## Slide 1: DAY 3 ROS
Navigation

## Slide 2
AGV in Factory
What’s ROS Navigation?
  ROS navigation Concept
Workshop AGV simulation
  Maps
  Move Base
  navigation
Workshop AGV
  Maps
  Move Base
  navigation
Milestone Day3

## Slide 3
What’s ROS Navigation?

## Slide 4
  AGV in Factory
https://www.youtube.com/watch?v=TKDtkkpsuiw

## Slide 5
  ROS navigation Concept
1
2
3
4
5
6

## Slide 6
  Hardware
Waffle
Lidar
Raspberry Pi
2x Wheel
2x Motor
2x Encoder
IMU
Driver
ESP32

## Slide 7: AGV HARDWARE (Overview)
  4x Mecanum Wheel (⌀ 12 mm)
  4x DC Motor 24 volt (90 RPM)
Battery 24 volt (15 Ah)
Controller
YDlidar G2
Mini PC
MICKY model 4
Notes: ส่วนแรกนะครับ คือ AGV hardware โดย AGV จะประกอบด้วย Hardware หลักๆ ดังนี้ครับ
Lidar สำหรับสร้างแผนที่ และระบบนำทาง
Mini PC เพื่อ run ROS master ซึ่งเป็นตัวประมวลผลหลักของ AGV
ระบบขับเคลื่อนใช้เป็น mecanum wheel แบบ 4 ล้อ ขับเคลื่อนด้วย มอเตอร์เกียร์ 90 rpm และแบตเตอรี่ 24 volt ครับ
Controller ครับ
อธิบายล้อ คืออะไร

## Slide 8: AGV HARDWARE (Controller)
Controller
4
2
2
3
3
5
1
6
1. Cucumber ESP32S2
► Support WIFI 2.4 GHz ► Secure boot
► Speed 240 MHz ► Low power
2. 2x Motor Driver
► Support 2 Channels ► 30A peak, 10 A cont.
► Support 5-30 volt ► Bi-directional
3. 4x Incremental ENCODER
► 400 P/R ► NPN open-collector
► 24 volt input ► 70 mA max
4. DFRobot IMU
► 3.3 – 5 volt input ► 3D Ang vel. ±250/500°/s
► 3D Acc. ±2/4/8/16g ► 3D Att ang. ±180°
5. RGB LED
► 4 – 7 volt input
► Support RGB lighting
6. Power input
► Fuse 24 volt
► 24 volt input
Notes: ส่วนของ controller ประกอบด้วย บอด cucumber ESP32S2 โดยมีข้อดีคือรองรับ wifi มีความเร็วในการประมวลผลสูงถึง 240 Hz สำหรับอ่านค่า sensor และควบคุมมอเตอร์ด้วย PID control
2 บอดมอเตอร์ Drive สำหรับควบคุมความเร็วมอเตอร์ 4 ตัว
3. Encoder สำหรับระบุตำแหน่ง AGV
4 IMU ระบุมุมของ AGV
5. LED แสดงสถานะของ AGV
และ Input ของบอดจะใช้ไฟ 24 volt จากแบตเตอรี่ครับ

## Slide 9
  1. Base controller
Get /cmd_vel
Calculate wheel target
Calculate wheel actual
PID controller
Run AGV
Topic “/cmd_vel” will be sent from “move base” to “base controller”
Type: geometry_msgs/Twist
Msgs:
Linear velocity x: 0.5
Linear velocity y: 0.5
Linear velocity z: 0.5
---
Angular velocity x: 0.0
Angular velocity y: 0.0
Angular velocity z: 0.1
Meter/sec
Radian/sec

## Slide 10
  1. Base controller
Get /cmd_vel
Calculate wheel target
Calculate wheel actual
PID controller
Run AGV
Linear.x
Angular.z
V = Linear.x
W = Angular.z
Meter/sec
Inverse kinematics

## Slide 11
  1. Base controller
Get /cmd_vel
Calculate wheel target
Calculate wheel actual
PID controller
Run AGV
Linear.x
Angular.z
Inverse kinematics

## Slide 12
  1. Base controller
Get /cmd_vel
Calculate wheel target
Calculate wheel actual
PID controller
Run AGV
Linear.x
Angular.z
Vr = target vel for right
Vl = target vel for left
“1000 pluse per round”
How to calculate wheel speed from encoder
Meter/sec

## Slide 13
  1. Base controller
Get /cmd_vel
Calculate wheel target
Calculate wheel actual
PID controller
Run AGV
Linear.x
Angular.z
Var = actual vel for right
Vla = actual vel for left
Vr = target vel for right
Vl = target vel for left
Cal target
Move base
/cam_vel
Σ
+
Vr
AGV
Driver
PWM 5v
PWM 24v
Encoder
-
Var
ESP32 controller
https://www.youtube.com/watch?v=NzunZLsuZ4k

## Slide 14
  1. Base controller
Get /cmd_vel
Calculate wheel target
Calculate wheel actual
PID controller
Run AGV
Linear.x
Angular.z
Var = actual vel for right
Vla = actual vel for left
Vr = target vel for right
Vl = target vel for left
PWM
https://www.youtube.com/watch?v=B_Ysdv1xRbA&t=12s

## Slide 15
  2. Odometry
B
A
X
Y
Encoder
IMU
How to calculate odometry

## Slide 16
  3. tf

## Slide 17
  4. scan
Lidar

## Slide 18
  5. Map

## Slide 19
  6. Move base
1
2
3
4
5
6

## Slide 20
Workspace AGV simulation
Fix “is not in the sudoers file. This incident will be reported”
https://www.baeldung.com/linux/username-not-in-sudoers-file
http://wiki.ros.org/catkin/Tutorials/create_a_workspace

## Slide 21
Workspace AGV simulation
Gazebo
RVIZ

## Slide 22
Workspace AGV simulation
Install ROS
Open terminal
$ :sudo sh -c 'echo "deb http://packages.ros.org/ros/ubuntu $(lsb_release -sc) main" > /etc/apt/sources.list.d/ros-latest.list’
$ : sudo apt install curl
$ : curl -s https://raw.githubusercontent.com/ros/rosdistro/master/ros.asc | sudo apt-key add –
$ : sudo apt update
$ : sudo apt install ros-noetic-desktop-full
$ : apt search ros-noetic
$ : source /opt/ros/noetic/setup.bash
$ : echo "source /opt/ros/noetic/setup.bash" >> ~/.bashrc
$ : source ~/.bashrc
$ : sudo apt install python3-rosdep python3-rosinstall python3-rosinstall-generator python3-wstool build-essential
$ : sudo apt install python3-rosdep
$ : sudo rosdep init
$ : rosdep update

## Slide 23
Workshop AGV simulation (installation)
Install Package for simulation and navigation
Open new terminal
$ : sudo apt install ros-noetic-dynamixel-sdk
$ : sudo apt install ros-noetic-turtlebot3-msgs
$ : sudo apt install ros-noetic-turtlebot3
$ : sudo apt install ros-noetic-slam-gmapping
$ : sudo apt install ros-noetic-navigation
$ : sudo apt-get install ros-noetic-teleop-twist-keyboard
$ : sudo apt install ros-noetic-tf2 ros-noetic-tf2-tools
Refer: https://github.com/ROBOTIS-GIT/turtlebot3
https://emanual.robotis.com/docs/en/platform/turtlebot3/simulation/

## Slide 24
Workshop AGV simulation (installation)
Install Node-js and Node-red
Open new terminal
Install Node-js
$ : curl -sL https://rpm.nodesource.com/setup_14.x | sudo bash --
$ : sudo apt install -y nodejs
Check
$ : node –v
$ : npm –v
Install Node-red
$ : sudo npm install -g --unsafe-perm node-red
Check
Open mew terminal
$ : node-red
Refer: https://www.arubacloud.com/tutorial/how-to-install-node-red-on-ubuntu-20-04.aspx

## Slide 25
Workshop AGV simulation (base controller)
Create Work Space
Check
$ :sudo nano ~/.bashrc
Open new terminal
$ :mkdir -p ~/sim_ws/src
$ : cd sim_ws
$ : catkin_make
$ : source devel/setup.bash
$ : source ~/sim_ws/devel/setup.bash
$ : echo source ~/sim_ws/devel/setup.bash >> ~/.bashrc

## Slide 26
Create agv Package
Check
$ :rospack list
Open new terminal
$ :cd sim_ws/src
$ : catkin_create_pkg agv_pkg std_msgs geometry_msgs rospy roscpp
$ : cd sim_ws
$ : catkin_make
Workshop AGV simulation (base controller)

## Slide 27
Create turtlebot3 Package
Check
$ :rospack list
Open new terminal
$ : cd sim_ws/src/
$ : git clone -b noetic-devel https://github.com/ROBOTIS-GIT/turtlebot3_simulations.git
$ : cd ~/sim_ws
$ : echo "export TURTLEBOT3_MODEL=waffle" >> ~/.bashrc
$ : catkin_make
Workshop AGV simulation (base controller)

## Slide 28
Test run base control node and simulation map
Open new terminal
$ : roscore
Open new terminal
$ echo "export TURTLEBOT3_MODEL=waffle" >> ~/.bashrc
$ roslaunch turtlebot3_gazebo turtlebot3_world.launch
Workshop AGV simulation (base controller)

## Slide 29
Test run base control node and simulation map
Open new terminal
$ : rostopic list
- /cmd_vel >>> command for base controller
- /odom >>> actual position for agv
- /scan >>> sensor data from lidar
- /tf >>> actual frame for agv,map,lidar
Workshop AGV simulation (base controller)

## Slide 30
Moving agv
Open new terminal
$ : rosrun teleop_twist_keyboard teleop_twist_keyboard.py
Workshop AGV simulation (base controller)

## Slide 31
Test msgs topic from agv
Open new terminal
$ : rostopic info /cmd_vel
Open new terminal
$ : rostopic info /scan
Open new terminal
$ : rostopic info /odom
Open new terminal
$ : rostopic info /tf
Workshop AGV simulation (base controller)

## Slide 32
Test msgs topic from agv
Open new terminal
$ : rostopic echo /cmd_vel
Open new terminal
$ : rostopic echo /scan
Open new terminal
$ : rostopic echo /odom
Open new terminal
$ : rostopic echo /tf
Workshop AGV simulation (base controller)

## Slide 33
  ROS navigation Concept
1
2
3
4
5
6
Next

## Slide 34
Workshop AGV simulation (gmapping)
Create gmapping_params.yaml
Create gmapping.rviz
Create bringup.launch
Create gmapping.launch
Create maps

## Slide 35
Workshop AGV simulation (gmapping)
Create param for ROS navigation
Open new terminal
$ : cd sim_ws/src/agv_pkg
$ : mkdir config maps param launch rviz
Check
$ :ls

## Slide 36
Workshop AGV simulation (gmapping)
Create param for ROS navigation
Open terminal
$ : cd sim_ws/src/agv_pkg/config
$ : touch gmapping_params.yaml
$ : sudo nano gmapping_params.yaml
map_update_interval: 2.0
maxUrange: 3.0
sigma: 0.05
kernelSize: 1
lstep: 0.05
astep: 0.05
iterations: 5
lsigma: 0.075
ogain: 3.0
lskip: 0
minimumScore: 50
srr: 0.1
srt: 0.2
str: 0.1
stt: 0.2
linearUpdate: 1.0
angularUpdate: 0.2
temporalUpdate: 0.5
resampleThreshold: 0.5
particles: 100
xmin: -10.0
ymin: -10.0
xmax: 10.0
ymax: 10.0
delta: 0.05
llsamplerange: 0.01
llsamplestep: 0.01
lasamplerange: 0.005
lasamplestep: 0.005
Copy this to gmapping_params.yaml
Ctrl + o >>> save
Ctrl + x >>> exit

## Slide 37
Workshop AGV simulation (gmapping)
Create rviz file for ROS navigation
Open terminal
$ : cd sim_ws/src/agv_pkg/rviz
$ : touch gmapping.rviz
$ : sudo nano gmapping.rviz
Check
$ : rviz
File > open config > select gmapping.rviz
Panels:
- Class: rviz/Displays
Help Height: 78
Name: Displays
Property Tree Widget:
Expanded:
- /TF1/Frames1
- /Map1
Splitter Ratio: 0.594406009
Tree Height: 715
- Class: rviz/Selection
Name: Selection
- Class: rviz/Tool Properties
Expanded:
- /2D Pose Estimate1
- /2D Nav Goal1
- /Publish Point1
Name: Tool Properties
Splitter Ratio: 0.588679016
- Class: rviz/Views
Expanded:
- /Current View1
Name: Views
Splitter Ratio: 0.5
- Class: rviz/Time
Experimental: false
Name: Time
SyncMode: 0
SyncSource: LaserScan
Visualization Manager:
Class: ""
Displays:
- Alpha: 0.5
Cell Size: 1
Class: rviz/Grid
Color: 160; 160; 164
Enabled: true
Line Style:
Line Width: 0.0299999993
Value: Lines
Name: Grid
Normal Cell Count: 0
Offset:
X: 0
Y: 0
Z: 0
Plane: XY
Plane Cell Count: 100
Reference Frame: map
Value: true
- Alpha: 1
Class: rviz/RobotModel
Collision Enabled: false
Enabled: true
Links:
All Links Enabled: true
Expand Joint Details: false
Expand Link Details: false
Expand Tree: false
Link Tree Style: Links in Alphabetic Order
base_footprint:
Alpha: 1
Show Axes: false
Show Trail: false
base_link:
Alpha: 1
Show Axes: false
Show Trail: false
Value: true
base_scan:
Alpha: 1
Show Axes: false
Show Trail: false
Value: true
caster_back_link:
Alpha: 1
Show Axes: false
Show Trail: false
Value: true
imu_link:
Alpha: 1
Show Axes: false
Show Trail: false
wheel_left_link:
Alpha: 1
Show Axes: false
Show Trail: false
Value: true
wheel_right_link:
Alpha: 1
Show Axes: false
Show Trail: false
Value: true
Name: RobotModel
Robot Description: robot_description
TF Prefix: ""
Update Interval: 0
Value: true
Visual Enabled: true
- Class: rviz/TF
Enabled: false
Frame Timeout: 15
Frames:
All Enabled: true
Marker Scale: 1
Name: TF
Show Arrows: true
Show Axes: true
Show Names: true
Tree:
{}
Update Interval: 0
Value: false
- Alpha: 1
Autocompute Intensity Bounds: true
Autocompute Value Bounds:
Max Value: 10
Min Value: -10
Value: true
Axis: Z
Channel Name: intensity
Class: rviz/LaserScan
Color: 0; 255; 0
Color Transformer: FlatColor
Decay Time: 0
Enabled: true
Invert Rainbow: false
Max Color: 255; 255; 255
Max Intensity: 11799
Min Color: 0; 0; 0
Min Intensity: 0
Name: LaserScan
Position Transformer: XYZ
Queue Size: 10
Selectable: true
Size (Pixels): 3
Size (m): 0.0300000007
Style: Flat Squares
Topic: /scan
Unreliable: false
Use Fixed Frame: true
Use rainbow: true
Value: true
- Class: rviz/Image
Enabled: false
Image Topic: /raspicam_node/image
Max Value: 1
Median window: 5
Min Value: 0
Name: Image
Normalize Range: true
Queue Size: 2
Transport Hint: compressed
Unreliable: false
Value: false
- Alpha: 0.699999988
Class: rviz/Map
Color Scheme: map
Draw Behind: false
Enabled: true
Name: Map
Topic: /map
Unreliable: false
Use Timestamp: false
Value: true
Enabled: true
Global Options:
Background Color: 48; 48; 48
Default Light: true
Fixed Frame: map
Frame Rate: 30
Name: root
Tools:
- Class: rviz/Interact
Hide Inactive Objects: true
- Class: rviz/MoveCamera
- Class: rviz/Select
- Class: rviz/FocusCamera
- Class: rviz/Measure
- Class: rviz/SetInitialPose
Topic: /initialpose
- Class: rviz/SetGoal
Topic: /move_base_simple/goal
- Class: rviz/PublishPoint
Single click: true
Topic: /clicked_point
Value: true
Views:
Current:
Angle: -1.57079637
Class: rviz/TopDownOrtho
Enable Stereo Rendering:
Stereo Eye Separation: 0.0599999987
Stereo Focal Distance: 1
Swap Stereo Eyes: false
Value: false
Invert Z Axis: false
Name: Current View
Near Clip Distance: 0.00999999978
Scale: 100
Target Frame: map
Value: TopDownOrtho (rviz)
X: 0
Y: 0
Saved: ~
Window Geometry:
Displays:
collapsed: false
Height: 1027
Hide Left Dock: false
Hide Right Dock: true
Image:
collapsed: false
QMainWindow State: 000000ff00000000fd00000004000000000000016a0000035cfc0200000009fb0000001200530065006c0065006300740069006f006e00000001e10000009b0000006600fffffffb0000001e0054006f006f006c002000500072006f007000650072007400690065007302000001ed000001df00000185000000a3fb000000120056006900650077007300200054006f006f02000001df000002110000018500000122fb000000200054006f006f006c002000500072006f0070006500720074006900650073003203000002880000011d000002210000017afb000000100044006900730070006c00610079007301000000430000035c000000df00fffffffb0000002000730065006c0065006300740069006f006e00200062007500660066006500720200000138000000aa0000023a00000294fb00000014005700690064006500530074006500720065006f02000000e6000000d2000003ee0000030bfb0000000c004b0069006e0065006300740200000186000001060000030c00000261fb0000000a0049006d006100670065000000020f000001900000001800ffffff000000010000010f0000035cfc0200000003fb0000001e0054006f006f006c002000500072006f00700065007200740069006500730100000041000000780000000000000000fb0000000a0056006900650077007300000000430000035c000000b800fffffffb0000001200530065006c0065006300740069006f006e010000025a000000b200000000000000000000000200000490000000a9fc0100000001fb0000000a00560069006500770073030000004e00000080000002e10000019700000003000004ff0000003efc0100000002fb0000000800540069006d00650100000000000004ff0000022400fffffffb0000000800540069006d006501000000000000045000000000000000000000038f0000035c00000004000000040000000800000008fc0000000100000002000000010000000a0054006f006f006c00730100000000ffffffff0000000000000000
Selection:
collapsed: false
Time:
collapsed: false
Tool Properties:
collapsed: false
Views:
collapsed: true
Width: 1279
X: 0
Y: 0
Copy this to gmapping.rviz
Ctrl + o >>> save
Ctrl + x >>> exit

## Slide 38
Workshop AGV simulation (gmapping)
Create bringup file for start gazebo
Open terminal
$ : cd sim_ws/src/agv_pkg/launch
$ : touch bringup.launch
$ : sudo nano bringup.launch
<launch> <!-- TurtleBot3 --> <include file="$(find turtlebot3_gazebo)/launch/turtlebot3_world.launch"> <arg name="model" value="waffle" /> </include> <!-- publish data --> <node pkg="robot_state_publisher" type="robot_state_publisher" name="robot_state_publisher">S <param name="publish_frequency" type="double" value="50.0" /> <param name="tf_prefix" value=""/> </node> </launch>
Copy this to bringup.launch
Ctrl + o >>> save
Ctrl + x >>> exit
Open new terminal
$ : roslaunch agv_pkg bringup.launch
Ctrl + c >>> exit

## Slide 39
Workshop AGV simulation (gmapping)
Create gmapping file for create maps
Open terminal
$ : cd sim_ws/src/agv_pkg/launch
$ : touch gmapping.launch
$ : sudo nano gmapping.launch
$ : cd sim_ws
$ : catkin_make
<launch> <!-- TurtleBot3 --> <include file="$(find agv_pkg)/launch/bringup.launch"> </include> <!-- Gmapping --> <node pkg="gmapping" type="slam_gmapping" name="gmapping_node" output="screen"> <param name="base_frame" value="base_footprint"/> <param name="odom_frame" value="odom"/> <param name="map_frame" value="map"/> <rosparam command="load" file="$(find agv_pkg)/config/gmapping_params.yaml" /> </node> <!-- Rviz --> <node pkg="rviz" type="rviz" name="rviz" required="true" args="-d $(find agv_pkg)/rviz/gmapping.rviz"/> </launch>
Copy this to gmapping.launch
Ctrl + o >>> save
Ctrl + x >>> exit
Open new terminal
$ : roslaunch agv_pkg gmapping.launch

## Slide 40
Workshop AGV simulation (gmapping)
Create maps
Open new terminal
$ : rosrun teleop_twist_keyboard teleop_twist_keyboard.py
Open new terminal
$ : rosrun map_server map_saver -f ~/sim_ws/src/agv_pkg/maps/mymap
Use I j k l ,
for moving

## Slide 41
Workshop AGV simulation (move base)
Create params.yaml
1. costmap_common_params.yaml ;2.dwa_local_planner_params.yaml ; 3. global_costmap_params.yaml ; 4. local_costmap_params.yaml ; 5. move_base_params.yaml
Create navigation.rviz
Create amcl.launch
Create move_base.launch
Create navigation.launch

## Slide 42
Workshop AGV simulation (move base)
Create param file for move base
Open terminal
$ : cd sim_ws/src/agv_pkg/param
$ : touch costmap_common_params.yaml dwa_local_planner_params.yaml global_costmap_params.yaml local_costmap_params.yaml move_base_params.yaml
$ : sudo nano costmap_common_params.yaml
obstacle_range: 3.0
raytrace_range: 3.5
footprint: [[-0.205, -0.155], [-0.205, 0.155], [0.077, 0.155], [0.077, -0.155]]
inflation_radius: 1.0
cost_scaling_factor: 3.0
map_type: costmap
observation_sources: scan
scan: {sensor_frame: base_scan, data_type: LaserScan, topic: scan, marking: true, clearing: true}
Copy this to costmap_common_params.yaml
Ctrl + o >>> save
Ctrl + x >>> exit
1

## Slide 43
Workshop AGV simulation (move base)
Create param file for move base
Open terminal
$ : sudo nano dwa_local_planner_params.yaml
DWAPlannerROS:
# Robot Configuration Parameters
max_vel_x: 0.26
min_vel_x: -0.26
max_vel_y: 0.0
min_vel_y: 0.0
# The velocity when robot is moving in a straight line
max_vel_trans: 0.26
min_vel_trans: 0.13
max_vel_theta: 1.82
min_vel_theta: 0.9
acc_lim_x: 2.5
acc_lim_y: 0.0
acc_lim_theta: 3.2
# Goal Tolerance Parameters
xy_goal_tolerance: 0.05
yaw_goal_tolerance: 0.17
latch_xy_goal_tolerance: false
# Forward Simulation Parameters
sim_time: 2.0
vx_samples: 20
vy_samples: 0
vth_samples: 40
controller_frequency: 10.0
# Trajectory Scoring Parameters
path_distance_bias: 32.0
goal_distance_bias: 20.0
occdist_scale: 0.02
forward_point_distance: 0.325
stop_time_buffer: 0.2
scaling_speed: 0.25
max_scaling_factor: 0.2
# Oscillation Prevention Parameters
oscillation_reset_dist: 0.05
# Debugging
publish_traj_pc : true
publish_cost_grid_pc: true
Copy this to dwa_local_planner_params.yaml
Ctrl + o >>> save
Ctrl + x >>> exit
2

## Slide 44
Workshop AGV simulation (move base)
Create param file for move base
Open terminal
$ : sudo nano global_costmap_params.yaml
global_costmap:
global_frame: map
robot_base_frame: base_footprint
update_frequency: 10.0
publish_frequency: 10.0
transform_tolerance: 0.5
static_map: true
Copy this to global_costmap_params.yaml
Ctrl + o >>> save
Ctrl + x >>> exit
3

## Slide 45
Workshop AGV simulation (move base)
Create param file for move base
Open terminal
$ : sudo nano local_costmap_params.yaml
local_costmap:
global_frame: odom
robot_base_frame: base_footprint
update_frequency: 10.0
publish_frequency: 10.0
transform_tolerance: 0.5
static_map: false
rolling_window: true
width: 3
height: 3
resolution: 0.05
Copy this to local_costmap_params.yaml Ctrl + o >>> save
Ctrl + x >>> exit
4

## Slide 46
Workshop AGV simulation (move base)
Create param file for move base
Open terminal
$ : sudo nano move_base_params.yaml
shutdown_costmaps: false
controller_frequency: 10.0
planner_patience: 5.0
controller_patience: 15.0
conservative_reset_dist: 3.0
planner_frequency: 5.0
oscillation_timeout: 10.0
oscillation_distance: 0.2
Copy this to move_base_params.yaml
Ctrl + o >>> save
Ctrl + x >>> exit
5

## Slide 47
Workshop AGV simulation (move base)
Create rviz file for ROS move base
Open terminal
$ : cd sim_ws/src/agv_pkg/rviz
$ : touch navigation.rviz
$ : sudo nano navigation.rviz
Check
$ : rviz
File > open config > select navigation.rviz
Panels:
- Class: rviz/Displays
Help Height: 78
Name: Displays
Property Tree Widget:
Expanded:
- /TF1/Frames1
- /TF1/Tree1
- /Global Map1/Costmap1
- /Global Map1/Planner1
- /Local Map1
- /Local Map1/Polygon1
- /Local Map1/Costmap1
- /Local Map1/Planner1
Splitter Ratio: 0.5
Tree Height: 783
- Class: rviz/Selection
Name: Selection
- Class: rviz/Tool Properties
Expanded:
- /2D Pose Estimate1
- /2D Nav Goal1
Name: Tool Properties
Splitter Ratio: 0.588679016
- Class: rviz/Views
Expanded:
- /Current View1
Name: Views
Splitter Ratio: 0.5
- Class: rviz/Time
Experimental: false
Name: Time
SyncMode: 0
SyncSource: LaserScan
Visualization Manager:
Class: ""
Displays:
- Alpha: 0.5
Cell Size: 1
Class: rviz/Grid
Color: 160; 160; 164
Enabled: true
Line Style:
Line Width: 0.0299999993
Value: Lines
Name: Grid
Normal Cell Count: 0
Offset:
X: 0
Y: 0
Z: 0
Plane: XY
Plane Cell Count: 20
Reference Frame: <Fixed Frame>
Value: true
- Alpha: 1
Class: rviz/RobotModel
Collision Enabled: false
Enabled: true
Links:
All Links Enabled: true
Expand Joint Details: false
Expand Link Details: false
Expand Tree: false
Link Tree Style: Links in Alphabetic Order
base_footprint:
Alpha: 1
Show Axes: false
Show Trail: false
base_link:
Alpha: 1
Show Axes: false
Show Trail: false
Value: true
base_scan:
Alpha: 1
Show Axes: false
Show Trail: false
Value: true
caster_back_link:
Alpha: 1
Show Axes: false
Show Trail: false
Value: true
imu_link:
Alpha: 1
Show Axes: false
Show Trail: false
wheel_left_link:
Alpha: 1
Show Axes: false
Show Trail: false
Value: true
wheel_right_link:
Alpha: 1
Show Axes: false
Show Trail: false
Value: true
Name: RobotModel
Robot Description: robot_description
TF Prefix: ""
Update Interval: 0
Value: true
Visual Enabled: true
- Class: rviz/TF
Enabled: false
Frame Timeout: 15
Frames:
All Enabled: false
Marker Scale: 1
Name: TF
Show Arrows: true
Show Axes: true
Show Names: false
Tree:
{}
Update Interval: 0
Value: false
- Alpha: 1
Autocompute Intensity Bounds: true
Autocompute Value Bounds:
Max Value: 10
Min Value: -10
Value: true
Axis: Z
Channel Name: intensity
Class: rviz/LaserScan
Color: 0; 255; 0
Color Transformer: FlatColor
Decay Time: 0
Enabled: true
Invert Rainbow: false
Max Color: 255; 255; 255
Max Intensity: 13069
Min Color: 0; 0; 0
Min Intensity: 28
Name: LaserScan
Position Transformer: XYZ
Queue Size: 10
Selectable: true
Size (Pixels): 3
Size (m): 0.0300000012
Style: Flat Squares
Topic: /scan
Unreliable: false
Use Fixed Frame: true
Use rainbow: true
Value: true
- Class: rviz/Image
Enabled: false
Image Topic: /raspicam_node/image
Max Value: 1
Median window: 5
Min Value: 0
Name: Image
Normalize Range: true
Queue Size: 2
Transport Hint: compressed
Unreliable: false
Value: false
- Alpha: 0.699999988
Class: rviz/Map
Color Scheme: map
Draw Behind: false
Enabled: true
Name: Map
Topic: /map
Unreliable: false
Use Timestamp: false
Value: true
- Alpha: 1
Buffer Length: 1
Class: rviz/Path
Color: 0; 0; 0
Enabled: true
Head Diameter: 0.300000012
Head Length: 0.200000003
Length: 0.300000012
Line Style: Lines
Line Width: 0.0299999993
Name: Planner Plan
Offset:
X: 0
Y: 0
Z: 0
Pose Color: 255; 85; 255
Pose Style: None
Radius: 0.0299999993
Shaft Diameter: 0.100000001
Shaft Length: 0.100000001
Topic: /move_base/NavfnROS/plan
Unreliable: false
Value: true
- Class: rviz/Group
Displays:
- Alpha: 0.699999988
Class: rviz/Map
Color Scheme: costmap
Draw Behind: true
Enabled: true
Name: Costmap
Topic: /move_base/global_costmap/costmap
Unreliable: false
Use Timestamp: false
Value: true
- Alpha: 1
Buffer Length: 1
Class: rviz/Path
Color: 255; 0; 0
Enabled: true
Head Diameter: 0.300000012
Head Length: 0.200000003
Length: 0.300000012
Line Style: Lines
Line Width: 0.0299999993
Name: Planner
Offset:
X: 0
Y: 0
Z: 0
Pose Color: 255; 85; 255
Pose Style: None
Radius: 0.0299999993
Shaft Diameter: 0.100000001
Shaft Length: 0.100000001
Topic: /move_base/DWAPlannerROS/global_plan
Unreliable: false
Value: true
Enabled: true
Name: Global Map
- Class: rviz/Group
Displays:
- Alpha: 1
Class: rviz/Polygon
Color: 0; 0; 0
Enabled: true
Name: Polygon
Topic: /move_base/local_costmap/footprint
Unreliable: false
Value: true
- Alpha: 0.699999988
Class: rviz/Map
Color Scheme: costmap
Draw Behind: false
Enabled: true
Name: Costmap
Topic: /move_base/local_costmap/costmap
Unreliable: false
Use Timestamp: false
Value: true
- Alpha: 1
Buffer Length: 1
Class: rviz/Path
Color: 255; 255; 0
Enabled: true
Head Diameter: 0.300000012
Head Length: 0.200000003
Length: 0.300000012
Line Style: Lines
Line Width: 0.0299999993
Name: Planner
Offset:
X: 0
Y: 0
Z: 0
Pose Color: 255; 85; 255
Pose Style: None
Radius: 0.0299999993
Shaft Diameter: 0.100000001
Shaft Length: 0.100000001
Topic: /move_base/DWAPlannerROS/local_plan
Unreliable: false
Value: true
Enabled: true
Name: Local Map
- Alpha: 1
Arrow Length: 0.0500000007
Axes Length: 0.300000012
Axes Radius: 0.00999999978
Class: rviz/PoseArray
Color: 0; 192; 0
Enabled: true
Head Length: 0.0700000003
Head Radius: 0.0299999993
Name: Amcl Particles
Shaft Length: 0.230000004
Shaft Radius: 0.00999999978
Shape: Arrow (Flat)
Topic: /particlecloud
Unreliable: false
Value: true
- Alpha: 1
Axes Length: 1
Axes Radius: 0.100000001
Class: rviz/Pose
Color: 255; 25; 0
Enabled: true
Head Length: 0.300000012
Head Radius: 0.100000001
Name: Goal
Shaft Length: 0.5
Shaft Radius: 0.0500000007
Shape: Arrow
Topic: /move_base_simple/goal
Unreliable: false
Value: true
Enabled: true
Global Options:
Background Color: 48; 48; 48
Default Light: true
Fixed Frame: map
Frame Rate: 30
Name: root
Tools:
- Class: rviz/MoveCamera
- Class: rviz/Interact
Hide Inactive Objects: true
- Class: rviz/Select
- Class: rviz/SetInitialPose
Topic: /initialpose
- Class: rviz/SetGoal
Topic: /move_base_simple/goal
- Class: rviz/Measure
Value: true
Views:
Current:
Angle: -1.57079637
Class: rviz/TopDownOrtho
Enable Stereo Rendering:
Stereo Eye Separation: 0.0599999987
Stereo Focal Distance: 1
Swap Stereo Eyes: false
Value: false
Invert Z Axis: false
Name: Current View
Near Clip Distance: 0.00999999978
Scale: 100
Target Frame: <Fixed Frame>
Value: TopDownOrtho (rviz)
X: 0
Y: 0
Saved: ~
Window Geometry:
Displays:
collapsed: false
Height: 1027
Hide Left Dock: false
Hide Right Dock: true
Image:
collapsed: false
QMainWindow State: 000000ff00000000fd00000004000000000000016a000003a0fc0200000007fb0000001200530065006c0065006300740069006f006e00000001e10000009b0000006600fffffffb0000001e0054006f006f006c002000500072006f007000650072007400690065007302000001ed000001df00000185000000a3fb000000120056006900650077007300200054006f006f02000001df000002110000018500000122fb000000200054006f006f006c002000500072006f0070006500720074006900650073003203000002880000011d000002210000017afb000000100044006900730070006c0061007900730100000043000003a0000000df00fffffffb0000000a0049006d0061006700650000000317000000cc0000001800fffffffb0000000a0049006d0061006700650000000330000000ce0000000000000000000000010000010f000003a0fc0200000003fb0000001e0054006f006f006c002000500072006f00700065007200740069006500730100000041000000780000000000000000fb0000000a005600690065007700730000000043000003a0000000b800fffffffb0000001200530065006c0065006300740069006f006e010000025a000000b200000000000000000000000200000490000000a9fc0100000001fb0000000a00560069006500770073030000004e00000080000002e10000019700000003000004a00000003efc0100000002fb0000000800540069006d00650000000000000004a00000022400fffffffb0000000800540069006d006501000000000000045000000000000000000000038f000003a000000004000000040000000800000008fc0000000100000002000000010000000a0054006f006f006c00730100000000ffffffff0000000000000000
Selection:
collapsed: false
Time:
collapsed: false
Tool Properties:
collapsed: false
Views:
collapsed: true
Width: 1279
X: 0
Y: 0
Copy this to navigation.rviz
Ctrl + o >>> save
Ctrl + x >>> exit

## Slide 48
Workshop AGV simulation (move base)
Create amcl (Monte Carlo localization approach)
Open terminal
$ : cd sim_ws/src/agv_pkg/launch
$ : touch amcl.launch
$ : sudo nano amcl.launch
<launch>
<!-- Arguments -->
<arg name="scan_topic" default="scan"/>
<arg name="initial_pose_x" default="0.0"/>
<arg name="initial_pose_y" default="0.0"/>
<arg name="initial_pose_a" default="0.0"/>
<!-- AMCL -->
<node pkg="amcl" type="amcl" name="amcl">
<param name="min_particles" value="500"/>
<param name="max_particles" value="3000"/>
<param name="kld_err" value="0.02"/>
<param name="update_min_d" value="0.20"/>
<param name="update_min_a" value="0.20"/>
<param name="resample_interval" value="1"/>
<param name="transform_tolerance" value="0.5"/>
<param name="recovery_alpha_slow" value="0.00"/>
<param name="recovery_alpha_fast" value="0.00"/>
<param name="initial_pose_x" value="$(arg initial_pose_x)"/>
<param name="initial_pose_y" value="$(arg initial_pose_y)"/>
<param name="initial_pose_a" value="$(arg initial_pose_a)"/>
<param name="gui_publish_rate" value="50.0"/>
<remap from="scan" to="$(arg scan_topic)"/>
<param name="laser_max_range" value="3.5"/>
<param name="laser_max_beams" value="180"/>
<param name="laser_z_hit" value="0.5"/>
<param name="laser_z_short" value="0.05"/>
<param name="laser_z_max" value="0.05"/>
<param name="laser_z_rand" value="0.5"/>
<param name="laser_sigma_hit" value="0.2"/>
<param name="laser_lambda_short" value="0.1"/>
<param name="laser_likelihood_max_dist" value="2.0"/>
<param name="laser_model_type" value="likelihood_field"/>
<param name="odom_model_type" value="diff"/>
<param name="odom_alpha1" value="0.1"/>
<param name="odom_alpha2" value="0.1"/>
<param name="odom_alpha3" value="0.1"/>
<param name="odom_alpha4" value="0.1"/>
<param name="odom_frame_id" value="odom"/>
<param name="base_frame_id" value="base_footprint"/>
</node>
</launch>
Copy this to amcl.launch
Ctrl + o >>> save
Ctrl + x >>> exit

## Slide 49
Workshop AGV simulation (move base)
Create move_base.launch
Open terminal
$ : cd sim_ws/src/agv_pkg/launch
$ : touch move_base.launch
$ : sudo nano move_base.launch
<launch>
<!-- move_base -->
<node pkg="move_base" type="move_base" respawn="false" name="move_base" output="screen">
<param name="base_local_planner" value="dwa_local_planner/DWAPlannerROS" />
<rosparam file="$(find agv_pkg)/param/costmap_common_params.yaml" command="load" ns="global_costmap" />
<rosparam file="$(find agv_pkg)/param/costmap_common_params.yaml" command="load" ns="local_costmap" />
<rosparam file="$(find agv_pkg)/param/local_costmap_params.yaml" command="load" />
<rosparam file="$(find agv_pkg)/param/global_costmap_params.yaml" command="load" />
<rosparam file="$(find agv_pkg)/param/move_base_params.yaml" command="load" />
<rosparam file="$(find agv_pkg)/param/dwa_local_planner_params.yaml" command="load" />
</node>
</launch>
Copy this to move_base.launch
Ctrl + o >>> save
Ctrl + x >>> exit

## Slide 50
Workshop AGV simulation (move base)
Create navigation.launch
Open terminal
$ : cd sim_ws/src/agv_pkg/launch
$ : touch navigation.launch
$ : sudo nano navigation.launch
<launch>
<!-- TurtleBot3 --> <include file="$(find agv_pkg)/launch/bringup.launch"> </include>
<!-- Map server -->
<node pkg="map_server" name="map_server" type="map_server" args="$(find agv_pkg)/maps/mymap.yaml"/>
<!-- AMCL -->
<include file="$(find agv_pkg)/launch/amcl.launch"/>
<!-- move_base -->
<include file="$(find agv_pkg)/launch/move_base.launch">
</include>
<!-- Rviz --> <node pkg="rviz" type="rviz" name="rviz" required="true" args="-d $(find agv_pkg)/rviz/navigation.rviz"/>
</launch>
Copy this to navigation.launch
Ctrl + o >>> save
Ctrl + x >>> exit

## Slide 51
Test RUN
Open new terminal
$ : roslaunch agv_pkg navigation.launch
Workshop AGV simulation (navigation)

## Slide 52
Set initial point for AGV
Workshop AGV simulation (navigation)

## Slide 53
Mark goal for AGV
Workshop AGV simulation (navigation)

## Slide 54
Workshop AGV simulation (move base)
Get current position of AGV
Open new terminal
$ : rosrun tf2_tools echo.py map base_footprint

## Slide 55
ROS with IoT (mqtt)
ROS with IoT (mqtt)

## Slide 56
ROS with IoT (mqtt)
Create mqtt.py
Open terminal
$ : cd sim_ws/src/agv_pkg/src
$ : touch mqtt.py
$ : sudo nano mqtt.py
$ : chmod +x mqtt.py
#!/usr/bin/env python3 import rospy from move_base_msgs.msg import MoveBaseAction, MoveBaseGoal import actionlib from actionlib_msgs.msg import * from tf.transformations import quaternion_from_euler from geometry_msgs.msg import Pose, Point, Quaternion import paho.mqtt.subscribe as subscribe import paho.mqtt.client as mqtt import json # mqtt connection host = '192.168.0.95' port = 1883 topic = '/ros_mqtt' time_out = 120 client = mqtt.Client() client.connect(host, port) rospy.loginfo(["connected"]) rospy.init_node('goal_nav', anonymous=False) move_base = actionlib.SimpleActionClient("move_base",MoveBaseAction) rate = rospy.Rate(20) # 5 hz rospy.loginfo("wait for the action server to come up") move_base.wait_for_server(rospy.Duration(5)) def mqtt(): global data rospy.loginfo(["waiting for sub"]) msg = subscribe.simple(topics=str(topic), hostname=host,port=port) rospy.loginfo(["Subed"]) data = json.loads(msg.payload.decode()) def movebase_client(): x = data.get('x') y = data.get('y') theta = data.get('th') x,y,theta = float(x), float(y), float(theta) #convert euler to quanternion q = quaternion_from_euler(0,0,theta) goal = MoveBaseGoal() goal.target_pose.header.frame_id = "map" goal.target_pose.header.stamp = rospy.Time.now() goal.target_pose.pose = Pose(Point(x, y, 0.000), Quaternion(q[0], q[1], q[2], q[3])) move_base.send_goal(goal) rospy.loginfo(["Going to goal"]) wait = move_base.wait_for_result(rospy.Duration(time_out)) state = move_base.get_state() if wait and state == GoalStatus.SUCCEEDED: result_stat = "OK" else: move_base.cancel_goal() result_stat = "Fail" rospy.loginfo(["Done result : " + result_stat]) def main(): while not rospy.is_shutdown(): mqtt() movebase_client() rate.sleep() if __name__ == '__main__': try: main() except rospy.ROSInterruptException: rospy.loginfo("Navigation finished.")
Copy this to mqtt.py
Ctrl + o >>> save
Ctrl + x >>> exit

## Slide 57
ROS with IoT (mqtt)
Open Firefox
Go to localhost:1880
Install node-red-contrib-aedes
Open new terminal
$ : pip install paho-mqtt

## Slide 58
ROS with IoT (mqtt)
Function 1:
var jsonData = { "x" : 2.070, "y" : -0.695, "th" : 1.606 }; msg.payload = jsonData; return msg;
Function 2:
var jsonData = { "x" : -0.379, "y" : 1.785, "th" : 3.039 }; msg.payload = jsonData; return msg;
Create function in node-red

## Slide 59
ROS with IoT (mqtt)
Open new terminal
$ : roscore
Open new terminal
$ : roslaunch agv_pkg navigation.launch
Open new terminal
$ : rosrun agv_pkg mqtt.py

## Slide 60
ROS with IoT (mqtt)
Open node-red
Click timestamp to sent goal
Test run with MQTT

## Slide 61
THANK YOU